## Slide 1: What is Computer Graphics?

## Slide 2: Computer Graphics
Computer graphics deals with all aspects of creating images with a computer
  Hardware
  Software
  Applications

## Slide 3: Objectives
In this lecture, we explore what computer graphics is about and survey some application areas
We start with a historical introduction

## Slide 4: Computer Graphics: 1950-1960
Computer graphics goes back to the earliest days of computing
  Strip charts
  Pen plotters
  Simple displays using A/D converters to go from computer to calligraphic CRT
Cost of refresh for CRT too high
  Computers slow, expensive, unreliable

## Slide 5: Computer Graphics: 1960-1970
Wireframe graphics
  Draw only lines
Sketchpad
Display Processors
Storage tube
wireframe representation
of objects

## Slide 6: Sketchpad
Ivan Sutherland’s PhD thesis at MIT
  Recognized the potential of man-machine interaction
  Loop
    Display something
    User moves light pen
    Computer generates new display
  Sutherland also created many of the now common algorithms for computer graphics

## Slide 7: Display Processor
Rather than have the host computer try to refresh display use a special purpose computer called a display processor (DPU)
Graphics stored in display list (display file) on display processor
Host compiles display list and sends to DPU

## Slide 8: Direct View Storage Tube
Created by Tektronix
  Did not require constant refresh
  Standard interface to computers
    Allowed for standard software
    Plot3D in Fortran
  Relatively inexpensive
    Opened door to use of computer graphics for CAD community

## Slide 9: Computer Graphics: 1970-1980
Raster Graphics
Beginning of graphics standards
  IFIPS
    GKS: European effort
      Becomes ISO 2D standard
    Core: North American effort
      3D but fails to become ISO standard
Workstations and PCs

## Slide 10: Raster Graphics
Image produced as an array (the raster) of picture elements (pixels) in the frame buffer

## Slide 11: Raster Graphics
Allows us to go from lines and wire frame images to filled polygons

## Slide 12: PCs and Workstations
Although we no longer make the distinction between workstations and PCs, historically they evolved from different roots
  Early workstations characterized by
    Networked connection: client-server model
    High-level of interactivity
  Early PCs included frame buffer as part of user memory
    Easy to change contents and create images

## Slide 13: Computer Graphics: 1980-1990
Realism comes to computer graphics
smooth shading
environment
mapping
bump mapping

## Slide 14: Computer Graphics: 1980-1990
Special purpose hardware
  Silicon Graphics geometry engine
    VLSI implementation of graphics pipeline
Industry-based standards
  PHIGS
  RenderMan
Networked graphics: X Window System
Human-Computer Interface (HCI)

## Slide 15: Computer Graphics: 1990-2000
OpenGL API
Completely computer-generated feature-length movies (Toy Story) are successful
New hardware capabilities
  Texture mapping
  Blending
  Accumulation, stencil buffers

## Slide 16: Computer Graphics: 2000-
Photorealism
Graphics cards for PCs dominate market
  Nvidia, ATI
Game boxes and game players determine direction of market
Computer graphics routine in movie industry: Maya, Lightwave
Programmable pipelines